## Slide 1: SMART ROOM CONTROLLER
By
Rodney Ham

## Slide 2
Notes: Manufacturing process has many control devices.

## Slide 3
Notes: Miles of wire connect devices to control panel. Problem: cracked/broken wires from friction resulting from conduit vibration; EMR exchange in conduit results in false readings; labor intensive to wire to floor of production equipment.

## Slide 4
Notes: Turn on flue fan to vent fumes

## Slide 5
Notes: Make sure there is no flue blockage by using a differential pressure meter

## Slide 6
Notes: Turn on water pump. Low water level shuts off burner. Quench products to proper temperature. Too hot of liquid results in improper hardening. Too cold causes fractures.

## Slide 7
Notes: Rotameter indicates visual of quench fluid flow.

## Slide 8
Notes: Ultrasonic meter measures amount of doping in quenching fluid.

## Slide 9
Notes: Pump starts to pressurize the gas

## Slide 10
Notes: Observe if furnace is at operating temperature

## Slide 11
Notes: Turn on IR detector for measuring temperature of molten material

## Slide 12
Notes: Fill hopper if low.

## Slide 13
Notes: Start conveyor.

## Slide 14
Notes: If furnace is at operating temperature grind material & feed into molds.

## Slide 15
Notes: Observe temperature of material leaving. Red led=too hot Clear led=desired range Blue led= material too cold.

## Slide 16
Notes: Check IR radiation of material in mold as it travels to hammers and presses. Rainbow lights indicate material approaching IR detector, directly under detector, moving away from detector. Adjust detector sensitivity (brightness of lights)

## Slide 17
Notes: Devices connected to internet via transmitters. No long wire runs.

## Slide 18
Notes: Devices connected to control panel via internet.

## Slide 19
Notes: Internet of Things controller simplifies the manufacturing line and increases production up time. No long wire runs. Less labor intensive. Fewer problems.